## Slide 1: GridAgent (Evaluation board) [Noah Klugman]
Purpose
  Evaluate sensors for the GridAgent board. GridAgent will provide ground truth power state information to the GridWatch central service over GSM and explore audio fingerprinting as a signal for grid state.
Specs
  Shield for Particle Electron
  MCU – STM32F205 (Electron)
    Cortex-M3
  Radio – U-Blox Sara G-Series (Electron)
    2G, $2.99/month for 1MB managed by Electron
  Memory
    128MB NOR Flash
  Sensors
    Hall effect - MLX90393ELW-ABA-011-SP, others TBD
    Light Sensor - ISL29035, others TBD
    Temperature/Humidity Sensor - SI7006-A20-IM, others TBD
    Microphones (PDM, stereo pair) - AKU441, SPH0641LU4H-1, MP34DB02TR, MP23AB02BTR
    CODEC - TBD.
  All remaining GPIO pins for Electron are broken out
  Program over USB or GSM
Documentation, hardware design files, software
  https://github.com/lab11/gridwatch/gridagent